ROTAFIX ENGINEERING ENQUIRY ESTIMATE

COMPANY - A R Services CONTACT- Les Varnon

TYPE C - SOLID TIMBER-RESIN SPLICE, TRS TOP SLOT KIT

CATEGORY - +/-3mm ENQ/JOB NO: 813

SITE - Theatre And Mill DATE - 07/08/2001

| C | REPAIR STEPS |
| --- | --- |

| 1 |  |
| --- | --- |

| 2 |  |
| --- | --- |

| 3 |  |
| --- | --- |

| 4 |  |
| --- | --- |

| 5 |  |
| --- | --- |

CONNECTION METHOD - RODS FACTORY FITTED INTO TRS UNIT - EPOXY/STEEL

(NB: 1 Slot illustrated only, for clarity)

Information specified by the Client:

Beam Reference Number

Timber Type

Number to Repair

Width (mm)

Depth (mm)

Overall Repair Length (mm)

1  of  2

SOFT

1

178

254

1524

The output data: (price inc. timber & resins)

Rod Overall Length (mm)

Rod Diameter (mm)

No. of Rods

No. of Slots

Slot Width (mm)

Slot Depth (mm)

Volume of resin, slot filling (L)

Price per beam kit

920

20

8

2

30

214

5.37

£480.92

TOTAL PRICE (1 off)

INC. 2.5L PACKS OF TG6

DELIVERY COST

£480.92

3

£63.61

(Rotafix 1997

Regardless of the repair system adopted, it can be a legal requirement to provide structural calculations to prove the validity of a proposed structural repair. It is the responsibility of the Contractor to discuss this issue with the Clients professional advisors. We will freely advise a Contractor on where independent structural calculations can be obtained from qualified Structural Engineers (£70 plus VAT, Indemnified, per connection)

See our INTERNET SITE at:

http://www.timber.org.uk/

or our Leaflet  (LDRT 1297/2)

David Moore - Property Repair Systems

Tel:	+44 (0)1626 331351

Fax:	+44 (0)1626 331143

e-mail:	dcmoore@timber.org.uk

(D C MOORE 1997

NO